## Slide 1
SIH 2026 • PROBLEM STATEMENT ISRO-01 • TEAM iTANTRA
iTantra
Ultra-Low Bitrate Offline Multilingual Walkie-Talkie & Tactical Emergency Mesh
Lightweight on-device STT + TTS for 10 Indian languages — no towers, no internet, no cloud. Speech in, voice out.
THEME Disaster Management & Tactical Emergency Comm.
CATEGORY Software — TinyML / Edge AI / Wireless Mesh
Team iTantra • SIH2026 / ISRO-01 • 1 / 6

## Slide 2
IDEA & INNOVATION
iTantra — Send Meaning, Not Audio
Speech
→
VAD
→
STT
→
≤38B Token
→
Mesh Tx
→
TTS
→
Voice
PROBLEM
• Voice audio too heavy for low-rate links.
• Text alerts exclude non-literate users.
• STT must fire on pauses, form sentences, stream instantly.
• Alerts must be voice: max-volume, non-interruptible.
• 10 languages, offline, on low-power phones.
OUR SOLUTION
• Silero pause-detect → dual-engine STT → sentence formation.
• Speech → ≤38 B token, ≈0.5 kbps: one UDP packet.
• Wi-Fi Direct / BT mesh; ChaCha20 + RS-FEC repair.
• Receiver TTS in own language; SOS siren override.
• PTT walkie-talkie / phone / SOS; 100% OSS, zero cloud.
WHY DIFFERENT
• Voice notes need internet + MBs; dead in blackouts.
• Radios: one language, no translation, extra hardware.
• Cloud STT: proprietary, needs network, leaks voice.
• Text-mesh excludes non-literate users.
• Single-model STT fails the south (CER 0.45–0.61).
KEY VALUE PROPOSITION • ≈256–512× less RF (0.5 kbps msg vs 128–256 kbps raw) • CER 0.03–0.34 • 467 + 15 tests green • APK 270 MB • CPU-only
★ Fine-tuning roadmap: P1 shipped (south-indic) → P2 Kathbath 1,700 h + Vaani 7,000 h → P3 synthetic disaster vocabulary
Team iTantra • SIH2026 / ISRO-01 • 2 / 6

## Slide 3
TECHNICAL APPROACH
Sender → mesh → receiver
16 kHz PCM → Silero VAD → Hybrid STT (Conformer / Whisper) → Semantic token ≤38 B → ChaCha20 + RS-FEC → UDP / Wi-Fi Direct / BT → TTS → Voice / Siren
STACK
• App + audio: Kotlin/Coroutines; C++20 + Oboe 16 kHz mono; JNI bridge.
• AI on CPU only: Silero VAD 2.3 MB + Conformer INT8 + whisper.cpp Q8_0; -O2, 4 threads.
• Store + forward: Protobuf frames, Room/SQLite audit log, background queue.
MODES & PACKET
• Modes: PTT walkie-talkie • normal chat • SOS siren broadcast.
• 38-B frame: header (node, lang, priority, time) + payload + CRC32.
• Survivability: RS(255,223) burst-loss recovery; Huffman tier; fragmentation.
Team iTantra • SIH2026 / ISRO-01 • 3 / 6

## Slide 4
FEASIBILITY & VIABILITY
Measured on-device, not slides
VALIDATION (measured)
• 467 backend + 15 integration tests green; Sep 2026 run (10 skipped); transport 4/4.
• ≤38 B payload (code MAX_FRAME_SIZE), ≈0.5 kbps/msg; Dravidian CER 0.05–0.34; hi 0.03.
• APK 270 MB (≤300 cap); device 3353f694 ADB-verified; CPU-only, power draw Not Yet Tested.
• Scales: 2-node PTT → 10-node team → multi-hop cluster.
RISKS → FIXES
• Small RAM phones → INT8/Q8_0 models + lazy load (gated langs only).
• Dialect errors → P2 fine-tune on Kathbath + Vaani corpora.
• Packet loss → RS-FEC parity + retries + fragmentation.
• Collisions / noise → CSMA/CA channel lock; VAD + noise gate pre-STT.
Team iTantra • SIH2026 / ISRO-01 • 4 / 6

## Slide 5
IMPACT & VALUE
Who gains, and how much
PEOPLE & OPS
• Social: voice-in/voice-out in 10 languages; works for non-literate users.
• Admin: NDRF/police/fire/medical coordinate cross-language; SOS siren override.
• Economic: runs on ordinary phones; zero cloud/data bills.
TRUST & NATION
• Privacy: voice never leaves the phone; open-source auditable stack.
• Green: ≈256–512× less RF (0.5 kbps msg vs 128–256 kbps raw); longer life for existing handsets.
• Atmanirbhar: indigenous stack, works through total grid/internet blackout.
Team iTantra • SIH2026 / ISRO-01 • 5 / 6

## Slide 6
RESEARCH & REFERENCES
Every claim traces to a source
PROBLEM + AI
• ITU emergency-telecom handbook; NDMA plan; ISRO/SIH-2026 PS.
• AI4Bharat IndicConformer + Kathbath (IIT-M).
• ARTPARK-Vaani 7,000 h Indic corpus (IISc) — P2 tuning data.
• parambharat/whisper-tiny-south-indic (HF) + whisper.cpp.
• Silero VAD — speech gating pre-STT.
MARKET + PROOF
• MarketsandMarkets, Critical Communications, Global, 2024: $18.4B (2024) → $34.8B (2030), 11.2% CAGR.
• TRAI Performance Indicators, India, 2024: ~1.19B wireless subscribers (Est., unverified here).
• iTantra audit, Sep 2026: 467 backend + 15 integration tests green; ≤38 B payload.
• STT_GATE_RESULTS.md, Sep 2026: laptop CER gate + on-device parity.
Team iTantra • SIH2026 / ISRO-01 • 6 / 6